## Slide 1: EE Systems integration & validation
SC2 Vision Door Control System
EE Systems test report

## Slide 2
High Level Summary
Design door system control for the SC2 Vision concept car. This includes high level system schematic, back-end logic control, hardware and software design.

## Slide 3
System Block Diagram
Mobile APP
Door Switches I/O
Exterior Lighting
Jrk1 Motor Controller
Linear Actuator
ESP32 (Arduino)
Driver Door
Jrk2 Motor Controller
Linear Actuator
Passenger Door
Hydraulic Pump

## Slide 4: Electrical System Schematic

## Slide 5: Electrical System

## Slide 6
Mobile APP Control
Mobile APP function | 
Driver/Passenger momentary open | Momentary open for each individual driver door. Hold button to keep opening. Release button press to stop
Driver/Passenger momentary close | Momentary close for each individual driver door. Hold button to keep closing. Release button press to stop
Driver/Passenger automatic open | Automatically will open driver/passenger door or both doors simultaneously.
Driver/Passenger automatic close | Automatically will close driver/passenger door or both doors simultaneously.
Hydraulic pump control | Momentary control for vehicle hydraulic pump. Increase or decrease the suspension height.
Mobile APP feedback | 
Door status position | Mobile app animation will reflect door actual door status
System error | Mobile app will display if any system error occurs. It will display if driver/passenger system error or both
Obstacle detected | If motor detects excess current above normal load +- tolerance, it will read as obstacle/person in the way and doors will stop moving

## Slide 7
Door Switch Control
Driver/Passenger switch function | 
Driver/Passenger Internal Switch | Automatic open or close for each door individually. Door will always automatically open all the way and will only close if previous position was full open.
Driver/Passenger External Switch | Automatic open or close for each door individually. Door will always automatically open all the way and will only close if previous position was full open.
Driver/Passenger Internal/External Switch | If switch is pressed while motor is moving, the switch will serve as a stop button.
Driver/Passenger
Internal Switch
External Switch

## Slide 8
Hydraulic Pump Control
12V
Up
Down
ESP32
3V->5V

## Slide 9
Hydraulic Pump Control Continued…
Hydraulic pump function | 
Momentary manual switch | Momentary “Up/Down” manual switch. This is a physical switch that will allow user to control hydraulic pump up and down. If the momentary switch is active, the 12V+ supply will be cut off from the “mobile app relay controls” to ensure no conflicting commands between physical switch and mobile app buttons.
Mobile App “UP” button | Mobile App will have a “Hydraulic Pump” control widget. The user can press the “Up” button to close relay and provide 12V+ to hydraulic pump. It is a momentary button, once button is released the relay will open and stop hydraulic pump.
Mobile App “DOWN” button | Mobile App will have a “Hydraulic Pump” control widget. The user can press the “Down” button to close relay and provide 12V- to hydraulic pump. It is a momentary button, once button is released the relay will open and stop hydraulic pump.

## Slide 10: Light Control
Light control function | 
Mobile APP lights on button | Turn on the Front/Rear lighting using mobile app. Light status will reflect on mobile app.
Mobile APP lights off button | Turn off the Front/Rear lighting using mobile app. Light status will reflect on mobile app.
ESP32
3V->5V
12V
Front/Rear LED Lighting

## Slide 11
The END